## Slide 1: A Method for Storing Semiconductor Test Data to Simplify Data Analysis
Jeremy W. Webb
J. Webb Consulting
jeremy.webb@jwebb-consulting.com

## Slide 2: Outline
Introduction
Data Producers and Consumers
Data Sources
Data Import
Database Structure
Data Analysis
Q&A

## Slide 3: Introduction
Developing a parametric database for storing semiconductor test data:
  Large volume of data
  Extracting useful information
  Analyzing data
Notes: This paper describes the steps necessary to develop a parametric database for storing semiconductor test data.
A large volume of data is generated during semiconductor fabrication, wafer testing, and package testing.
Extracting any useful information from this collection of files can be challenging.
Custom scripts, Excel spreadsheets, R, GNU Plot scripts employed to make sense of data for performance and yield analysis.

## Slide 4: Parametric Database Design
Interviews
Producers
Consumers
Sources
Design
Foundry
Import
XML
Load Scripts
Production
Database
Structure
Relationships
Analysis
Yield
Performance
Reports
Automation
Views

## Slide 5: Data Producers
IC Design and Test Engineers
Wafer Foundries
Test Executive Software
Who or What Produces Data?
Common Questions
What type of data do you generate?
Where do you store data?
What type of specifications exist for devices?

## Slide 6: Data Consumers
IC Design, Test, and Quality Engineers
Managers and Production Planners
Test Executive Software
Who or What Consumes Data?
Common Questions
What type of data do you access? Where do you access data?
Do you have to reformat data prior to analysis?

## Slide 7: Data Sources Design Data
GDSII Documentation Layer
  Describes reticle makeup, including row/column positions of each DUT.
  Reticle row/column positions translated into wafer level X/Y coordinates.
  ChipID for each DUT calculated using wafer level X/Y coordinates.
  ChipID used to link measurement data with appropriate DUT.
Notes: GDSII files are difficult to parse, tends to be an iterative process.

## Slide 8: Data Sources Design Data – Process

## Slide 9: Data Sources Design Data – XML File
<?xml version="1.0" encoding="UTF-8"?>
<mask>
<info>
</info>
<mask_params>
</mask_params>
<gdsii>
</gdsii>
<reticle>
</reticle>
<dut id="DEV-01">
</dut>
<die id="A5500">
</die>
</mask>
<info>
<mask_name>aa001</mask_name>
<timestamp>1404616217</timestamp>
<material>gaas</material>
<device_type>wafer</device_type>
<makeup>whole</makeup>
<foundry>foundry1</foundry>
</info>
<mask_params>
<x_width>150000.0</x_width>
<y_height>150000.0</y_height>
<center_column>4.0</center_column>
<center_row>4.0</center_row>
<x_offset>0.0</x_offset>
<y_offset>7.0</y_offset>
<rim_scale>1.2</rim_scale>
<max_reticle_cols>9.0</max_reticle_cols>
<max_reticle_rows>8.0</max_reticle_rows>
<wafer_x_offset>-1000.0</wafer_x_offset>
<wafer_y_offset>0.0</wafer_y_offset>
<inner_ring>0.96</inner_ring>
<middle_ring>0.98</middle_ring>
<outer_ring>1.0</outer_ring>
<pcm_xoffset>0.0</pcm_xoffset>
</mask_params>
<gdsii>
<filename>mychip.gds</filename>
<filesize>51200</filesize>
<filepath>/prod/wafer/mychip/</filepath>
<fileblob><snip></fileblob>
<filedump><snip></filedump>
<timestamp>1404616217</timestamp>
<quadrant>Q</quadrant>
</gdsii>
<reticle>
<width>18400</width>
<height>21320</height>
<scale>0.00000100</scale>
<units>meters</units>
<makeup>whole</makeup>
</reticle>
<dut id="DEV-01">
<dut_key>DEV-01</dut_key>
<dut_family>DEV</dut_family>
<dut_type>01</dut_type>
<dut_x>920</dut_x>
<dut_y>1640</dut_y>
</dut>
<dut id="PCM-01">
<dut_key>PCM-01</dut_key>
<dut_family>PCM</dut_family>
<dut_type>01</dut_type>
<dut_x>920</dut_x>
<dut_y>1640</dut_y>
</dut>
<die id="A5500">
<die_key>DEV-01</die_key>
<die_family>DEV</die_family>
<die_type>01</die_type>
<die_quadrant>A</die_quadrant>
<die_x>73600</die_x>
<die_y>63960</die_y>
<die_edge>0</die_edge>
</die>
<die id="snip">
</die>
<die id="D5501">
<die_key>DEV-01</die_key>
<die_family>DEV</die_family>
<die_type>01</die_type>
<die_quadrant>D</die_quadrant>
<die_x>74520</die_x>
<die_y>63960</die_y>
<die_edge>0</die_edge>
</die>

## Slide 10: Data Sources Foundry Data
Data Types:
  Open Purchase Orders
  Work In Progress Status
  Process Control Monitor Data
  Wafer Level Test Data
Header Information
  Wafer mask name
  Wafer lot number or identifier
  Wafer number
  Test station identifier
  Test date and time
  Measurement conditions
Notes: Open PO:
  Indicates new masks or wafer lots in the pipeline
WIP:
  Process of wafer fabrication and testing,
  An interesting observation during the dB development was that the process steps vary from wafer to wafer.
PCM Data:
  Performance of PCM circuits on wafer mapped to XY Coordinates
Wafer Test:
  Functional Test results mapped to XY Coordinates
  Work with foundry to ensure proper meta data is stored in header of test results and that the format stays consistent to avoid breaking parsing scripts.
  Always include a file format version number!
  Ask them to include specifications for each measured parameter.
If device test data is provided in separate files (aka, Swept Measurement Data), then the ChipID should also be included.

## Slide 11: Data Sources Foundry Data – Process

## Slide 12: Data Sources Production Data
Intermediate Data Storage
  Combined File (e.g., CSV or Excel)
  Separate Files
  Database (i.e., session or production)
Data Types
  Parametric Test Data
  Swept Measurement Data
Notes: Intermediate Data Storage
  Combined Files
    Problems exist when test runs start/stop. Never a cohesive file and manual merging is typically required.
  Separate Files
    Typical format is a custom flat file with structure (aka, sections containing info, specs, measurements)
  Database
    Session dB can be a SQLite dB file.
    Production dB would be the MySQL/MariaDB dB hosted on a remote server.
Data Types
  Parametric Test Data
    Contain discrete measurement data.
    Typically thousands of files or rows in spreadsheet or dB per wafer.
  Swept Measurement Data
    Network Analyzer Touchstone Files (*.s2p, *.s4p, *.sNp)
    Typically thousands of files.
    Number of frequency points per sweep can vary.

## Slide 13: Data Sources Production Data – Process

## Slide 14: Data Sources Production Data – Parametric Test Data
<?xml version="1.0" encoding="UTF-8"?>
<die_data>
<info>
</info>
<specifications>
<spec_class id="DEV-01">
<specification id="Ambient">
</specification>
</spec_class>
</specifications>
<measure>
<measure_class id="DEV-01">
<parameter id="Ambient Temperature">
</parameter>
</measure_class>
</measure>
</die_data>
<info>
<file_version>1.1</file_version>
<username>jwwebb</username>
<timestamp>1404616217</timestamp>
<mask_name>aa001</mask_name>
<lot_number>1</lot_number>
<wafer_id>1</wafer_id>
<quadrant>q</quadrant>
<device_type>wafer</device_type>
<material>gaas</material>
<dut_family>DEV</dut_family>
<dut_type>01</dut_type>
<dut_chipid>A5500</dut_chipid>
<dut_status>PASSED</dut_status>
<test_sequence>first-pass</test_sequence>
<test_system>TS10</test_system>
<test_type>final_test</test_type>
</info>
<specifications>
<spec_class id="DEV-01">
<specification id="Ambient">
<spec_low_value>15</spec_low_value>
<spec_high_value>35</spec_high_value>
<spec_units>degC</spec_units>
<spec_desc>Ambient Temperature</spec_desc>
<spec_type>parameter</spec_type>
</specification>
<specification id="Idss">
<spec_low_value>0.22</spec_low_value>
<spec_high_value>0.33</spec_high_value>
<spec_units>Amps</spec_units>
<spec_desc>Drain Current</spec_desc>
<spec_type>parameter</spec_type>
</specification>
</spec_class>
</specifications>
<measure>
<measure_class id="DEV-01">
<parameter id="Ambient Temperature">
<param_value>21.264</param_value>
<param_units>degC</param_units>
<param_cond>Vg=0.0, Vd=8</param_cond>
<param_status>passed</param_status>
</parameter>
<parameter id="Idss">
<param_value>0.2869048</param_value>
<param_units>Amps</param_units>
<param_cond>Vg=0.0, Vd=8</param_cond>
<param_status>passed</param_status>
</parameter>
</measure_class>
</measure>

## Slide 15: Data Sources Production Data – Swept Measurement Data
<?xml version="1.0" encoding="UTF-8"?>
<touchstone>
<info>
</info>
<sparameters>
<data_row id="100000000">
</data_row>
<data_row id="snip">
</data_row>
</sparameters>
</touchstone>
<info>
<mask_name>aa001</mask_name>
<username>jwwebb</username>
<timestamp>1404616217</timestamp>
<material>gaas</material>
<quadrant>q</quadrant>
<lot_number>1</lot_number>
<wafer_id>1</wafer_id>
<device_type>wafer</device_type>
<dut_family>DEV</dut_family>
<dut_type>01</dut_type>
<dut_status>FAILED</dut_status>
<dut_chipid>A5500</dut_chipid>
<test_sequence>single-pass</test_sequence>
<test_system>TS10</test_system>
<test_type>final_test</test_type>
<option_line># HZ S RI R 50</option_line>
</info>
<sparameters>
<data_row id="100000000">
<freq>100000000</freq>
<s11_im>0.02047161</s11_im>
<s11_re>-0.04349013</s11_re>
<s12_im>-0.0001343436</s12_im>
<s12_re>1.809457e-05</s12_re>
<s21_im>1.051201</s21_im>
<s21_re>-3.672653</s21_re>
<s22_im>0.07070011</s22_im>
<s22_re>-0.1499106</s22_re>
</data_row>
<data_row id="snip">
</data_row>
</sparameters>

## Slide 16: Data Import Production Data
XML Root Element Detection
Common XML Child Elements
  info – describes the data in the XML file
  specifications – describes the pass/fail criteria
  measure – contains the measurement data
Batch Import Scripts
  Bottom up approach for discrete test files
Staged Import
  Manually performed tests
  Data generated from legacy systems
  Either nightly or “hot” staging
Notes: XML Root Element Detection
  Is it a mask, PCM data, test data, etc.
Common XML Child Elements
  info – Describes the data within the XML file (aka, material, device type, ChipID
Batch Import Scripts
  Bottoms up approach; develop import scripts for single file, then develop script to import all files in a specific directory, then develop script to import a list of directories
Staged Import: Web Based Staging Form
  Manual tests generate no trigger that data is ready for upload into the database.
  Augmenting legacy systems to directly import into a database may be difficult or impossible.
  Data staged for nightly imports occur at regular time slots on a daily basis (i.e., cron job running nightly at 10pm)
  Data staged for “hot” import should occur within a very narrow time range (i.e., cron job running every 30 minutes to an hour to determine if data is available for “hot” import).

## Slide 17: Data Import Foundry Import
FTP sites
  Foundry hosted
  Locally hosted
Conventions
  File name generation
  Compressed file directory structure
Foundries can accommodate requests to store additional information in FTP sites or to transfer data in your local FTP site.
Notes: FTP Sites are typically used to distribute PCM and functional test data
If not, then request that either an FTP site be created or create your own and have them push data to your site upon completion of any testing.
Agree on file naming conventions and compressed file structure (if used) to simplify parsing/import operations
Request access to open purchase orders, work in progress, PCM data, and wafer level test data via FTP.

## Slide 18: Database Structure Table Creation
Initial tables created after user interviews.
Table relationships refined over time.
Table Types:
  System Tables
  Map Tables
  Wafer Tables
Database IDEs, such as NaviCat®, are convenient for visualizing the table structure.

## Slide 19: Database Structure Model

## Slide 20: Data Analysis
Parametric database is accessed via ODBC.
Data analysis is performed by querying the tables and views.
Third party tools:
  R
  JMP® from SAS
  Matlab® from Mathworks
  Microsoft Excel®
  Scripting Languages, such as: Perl and Python

## Slide 21: Questions
Thank You!
Jeremy W. Webb
J. Webb Consulting
jeremy.webb@jwebb-consulting.com